## Slide 1: Low Latency Polar FEC Chain Development in Software for 5G Final thesis presentation
Yadhunandana R. Kumaraiah (Yadhu)
yadhu.kumaraiah@tum.de
Supervisors:
Fabian Steiner, Peihong Yuan (TUM)
Dr. Moritz Harteneck, Alexander Heinz
(Rohde & Schwarz)

## Slide 2: Agenda
Motivation
Background
Encoding FEC chain
Latency results : Encoding chain
Decoding FEC chain
Latency results : Decoding chain
Conclusion and Outlook

## Slide 3: Motivation
Traditionally FEC chains are developed with FPGA’s or ASIC’s to achieve low latency and high throughput.
Development/maintenance in FPGA/ASIC requires more time and expensive.
Due to the recent advances in General Purpose Processors, it is possible to achieve required latency with software implementations without custom hardware.
Software implementations require less development/maintenance effort and provide flexibility/ease of maintenance to device manufacturer.
However algorithms need to adopted/optimized to efficiently implement in software.

## Slide 4: Background: Polar Codes
Invented by Erdal Arıkan[1] in 2009.
First codes to theoretically approach channel capacity for BMC channels with explicit construction.
Basic idea is synthesizing either completely noiseless or noisy channels based on SNR.
Information bits are transmitted in noiseless and zeros in noisy channels .
Synthesizing channels for every SNR is complex. 5G adopted heuristic low complexity approach independent of SNR[2] .
This construction performs sufficiently good over a large range of SNR[1]
Encoder circuit for
,
Fraction of good channels
Butterfly circuit

## Slide 5: Polar Encoding (Polar Transform)
XOR introduces correlation between code word bits.
Bits shown in red are frozen bits (zeros).
Node operation in encoder with vector size .
      //Superfluous copying
XOR operation
.
Each stage contains vector of size

## Slide 6: Decoding Polar Codes
Decoder estimates the code word by exploiting the correlation introduced by encoder.
Decoding involves Check Node (CN), Variable Node (VN) and bit combination operations.
Every node in the decoder tree performs these operations.
Decoding circuit can also be viewed as binary tree.
Each stage contains vector of size

## Slide 7: CN, VN and Bit Combination Operations
For LLR vector size
CN operation: ()
VN operation: ( )
        =
Bit combination:
Local decoder with messages

## Slide 8: Fast-SSC Algorithm
Fast-SSC algorithm[1] identifies special component codes from polar code which allow immediate decoding avoiding full tree traversal.
Reduces number of CN and VN operations.
Parallelizes the decoding operation.
Example
Original decoder tree
Reduced tree

## Slide 9: Processor Architecture
Cache memory
  Performance bottleneck in modern processors is accessing main memory.
  Modern processors have faster memory called cache.
  Caches reduce the average memory access latency by storing recently accessed data.
Instruction pipelining
  Modern processors come with advanced pipelining.
  Pipelining increases IPC (Instructions Per Cycle).
  Branching and cache misses create stalls in pipelining which reduce IPC. They should be reduced to achieve good performance.

## Slide 10: Vector Processing Units
Process multiple data elements (vectors) in a single instruction. Incorporated in modern processors.
Allow data parallelism, popular among video/image processing community.
Faster encoding/decoding in communication systems can be implemented using SIMD (Single instruction multiple data) instructions.
SIMD feature allows encoding/decoding with low latency.

## Slide 11: Encoding FEC Chain in 5G
FEC chain of Physical Broadcast Channel (PBCH) and Physical Downlink Control Channel (PDCCH).

## Slide 12: Polar Code Construction
Reliable bit indices need to be selected by considering effect of rate matching on reliability values.
Due to this dependency reliability indices selection process involves search and remove operations in the list, which have huge overhead. (377 μs in the functional implementation).
Algorithm reformulated to use lookup table and mark the elements instead of removing.
Reformulated algorithm avoids redundant copying, search and remove operations. Latency reduced to 15 μs.

## Slide 13: Optimization of Polar Encoder
Avoid superfluous copying:
  Intelligent memory layout design for
Exploit data parallelism:
  Naive implementation in software considers each bit as one integer. Each bit is processed sequentially.
  Multiple bits processed in parallel by packing multiple bits to single integer. E.g. int8 = 8 info bits, int64 = 64 info bits.
  SIMD registers are 256 bits wide, Resulting in a parallelism factor . SIMD processors come with fast pack/unpack instructions.
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Each row represents 8 bit integer representing one info bit.
Only last column contains info bits
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
8 bits grouped as one integer.

## Slide 14: Tree Pruning and Unrolling Recursion
Plain encoder implementation traverses till the end of tree. E.g.: , encoder needs to traverse nodes.
Pruning is done by building a lookup table and stopping encoding at level, i.e. 7 in our example.
Number of nodes reduced to 255 from 2047 hence significantly reducing the latency.
This optimization is applicable for hardware implementations as well.
Recursive function has overhead since every function call requires new stack allocation and branching. Both have huge overhead.

## Slide 15: Encoding Chain Results
Comparison with open source encoder software implementation (on AMD EPYC processor running at 1.6GHz)
Naive | Optimized
451 μs | 40 μs
Naive | Optimized
34 μs | 0.24 μs
Worst case encoding FEC chain:
Encoder Latency:
aff3ct[1] (No SIMD) | Current implementation
5.6 μs | 0.24 μs
Notes: Functional implementation done by colleague at R&S.
For FPGA implementation, value is scaled according to N value.

## Slide 16: Decoding FEC Chain
Decoding FEC chain for Uplink Control Information (UCI)

## Slide 17: Sub-block Deinterleaver
Inverse of subblock interleaver operation performed at the transmitter.
Deinterleaving is performed as shown in the figure.
Expensive operation due to huge number of division, multiplication and modulus operations and it is also sequential.
This operation is broken down into three parts, each of them are implemented using permute and blend SIMD instructions.
Latency reduced from 19to 0.47.

## Slide 18: Decoding: Optimized CN, VN and Bit Combination
Decoding operation involves CN, VN and bit combination instructions in every node of decoding tree.
Efficient implementation of these operations is critical for achieving low latency.
CN, VN and bit combination operations are vectorized.
Sign multiplication in CN operation is reduced to bitwise negation and implemented using SIMD instructions.
In VN operation multiplication based on is reformulated using bit wise negation.
Bit combination is performed with SIMD XOR instructions.
Avoiding superfluous copying:
    Intelligent memory layout design for so that it is part of without explicit copying.
CN operation: ()
VN operation:
        =
Bit combination:

## Slide 19: Packing Frozen Pattern
Packing multiple frozen bits allows efficient identification of component codes.
Frozen pattern is passed in packed bit format to decoder.
Identification component codes is performed at run time.
Packing of multiple bits together allows identification of component codes in a single comparison instruction.
Reduces the expensive branch instructions and exploits data parallelism.
For frozen pattern at child node = {1,1……..1,1} //256 values.
bool isRateZeroNode(int8_t frozenPattern[])
{
bool rateZeroNode = true;
for(auto i = 0; i < 256;i++) {
if(frozenPattern[i] != 1) {
rateZeroNode = false;
break;
}
}
return rateZeroNode;
}
Naive way
Efficient SIMD way
template<>
inline bool isRateZeroNode(uint64_t s[]) {
__m256i temp1 = _mm256_loadu_si256 ((__m256i*)s);
__m256i temp2;
temp2 = _mm256_set1_epi8 ((char)0xFF);
__m256i pcmp = _mm256_cmpeq_epi64 (temp1, temp2);
unsigned bitmask = _mm256_movemask_epi8(pcmp);
return (bitmask == 0xffffffffU);
}

## Slide 20: Decoding R0 and R1 Nodes
Decoding R0 code
  R0 node contains all frozen bits.
  Decoded bits are set to zero. Further tree traversal isn’t necessary.
Decoding R1 code
  R1 node contains all information bits.
  No extra information is gained by traversing full tree.
  Simple hard decision decoding is performed at this node.
  Decoding performed by applying threshold detection and polar transform.
To speedup R1 node decoding, threshold detection and polar transform is vectorized with a parallelism factor of 16 ()
Processes vectors of size 16 using SIMD instructions. Namely with vpcmpeq and vpxor.

## Slide 21: Decoding RPC Node
RPC node’s right most descendent contains information and all remaining bits are frozen.
Decoding operation involves summing of all the elements of LLR vector and deciding the bit based on the sum.
Result is stored at information bit position and zeros are stored in frozen bit positions.
Summation is calculated block wise with AVX2 vector instructions.

## Slide 22: Decoding SPC Node
SPC node’s left most descendent is a frozen bit and remaining positions contain information bits.
Decoding involves threshold detection, parity calculation, searching minimum magnitude LLR and polar transform.
Block wise threshold detection with SIMD comparison instruction.
Parity calculation with bit packing and POPCNT instruction.
Searching is performed with another SIMD instruction phminpos.
Finally optimized polar transform function is called.
SPC decoding
Threshold detection
PHMINPOS
Instruction
SIMD Comparison
POPCNT instruction
Polar
Transform
Searching
Parity
compute
SIMD XOR operation
Notes: position searching, polar transform
Parity calculation,

## Slide 23: Decoder Tree Pruning and Unrolling Recursion
Tree pruning
  Decoding latency can be further reduced by intelligently pruning the decoder tree. Pruning irrespective of frozen pattern.
  Latency reduction comes at the cost of increased BLER.
  High SNR and low code rate scenarios this method can be used. Level of pruning and BLER can be dealt as trade-off.
Unrolling recursion
  Recursion suits hardware implementation. However in software, it has a huge overhead.
  Decoder implementation is unrolled using templates concept of C++.
  With templates, compiler automatically generates the code for different vector sizes.

## Slide 24: CRC Calculation
Encoding FEC chain need to calculate CRC24 for downlink control information transmission.
Decoding FEC chain calculates CRC6 or CRC11 for CRC check.
CRC calculation is one of the significant latency contributor to both encoding and decoding FEC chains.
Processing individual bits for CRC calculation is very inefficient.
Extended the popular CRC algorithm[1] to calculate CRC24, CRC6 and CRC11 .
In this algorithm, 8 bits are processed in parallel rather than bit by bit,
Reduced CRC calculation latency from 8 μs to 0.8 μs in FEC chain.

## Slide 25: Miscellaneous Optimizations
Replaced multiplication/division and modulus operations with bitwise operations which achieve the same result
Implemented approximate versions logarithm and exponential functions to reduce the number of floating point multiplications.
Reduced the usage of jump functions to avoid flushing of the instruction pipeline, instead latest instruction extension CMOV is used.
Used the compiler optimization primitives for better instruction scheduling.
Cache Prefetching
  VN, CN and bit combination operations fetch a block of memory and access pattern is predictable.
  Memory access latencies reduced by fetching cache well in advance.
  Cache line fetched with PREFETCH instruction provided by 3dnow extension of EPYC processor.
Processor
L1-Cache
L2-Cache
L3-Cache
Main memory
Prefetching request
Data transfer

## Slide 26: Decoding Chain Results
Comparison with state of the art polar decoder software implementation (in AMD EPYC processor at 1.6 GHz)
Naive | Optimized
391 μs | 40 μs
[1]* | This work
8 μs | 5 μs
Worst case latency decoding FEC chain:
*Scaled according to frequency
Naive | Optimized
283.4 μs | 5 μs
Decoder latency:
Decoder latency compared to state of the art
State of the art : 8-bit LLRs
This work: 16-bit LLRs

## Slide 27: Conclusion
Both encoding and decoding FEC chains are efficiently implemented, achieved latency requirements through both algorithmic and software optimizations
Optimized implementation exploits modern features. Namely SIMD, Cache prefetching etc.
Achieved latency reduction of 10x.
Outlook
CRC aided Successive Cancellation List (CA-SCL) algorithm is also implemented. However it is not optimized.
CA-SCL algorithm has approximately 1.5dB gain over fast-SSC algorithm for N = 2048 and list size of 8[1].
Future work: Extend decoding FEC chain with optimized CA-SCL.

## Slide 28: Thank you
Questions
Naive | Optimized
391 μs | 40 μs
[1]* (8-bit LLR) | This work (16-bit LLR)
8 μs | 5 μs
Worst case latency decoding FEC chain:
Naive | Optimized
283.4 μs | 5 μs
Improvement in decoder latency:
Decoder latency compared to state of the art
Naive | Optimized
451 μs | 40 μs
Naive | Optimized
34 μs | 0.24 μs
Worst case encoding FEC chain:
Encoder Latency:
Decoding Chain results:
Encoding Chain results: