## Slide 1: Polar FEC development in software for NR(5G)
Yadhunandana Rajathadripura Kumaraiah
yadhunandana.kumaraiah@rohde-schwarz.com
COMPANY RESTRICTED

## Slide 2: Contents
Polar Encoding Background
5G polar encoding chain
Latency measurement.
Code profiling
Polar encoder latency.
Polar code construction and optimization.
Polar transform optimization.
Optimal CRC calculation.
Current status.
Research directions.
References.
COMPANY RESTRICTED

## Slide 3: Polar Codes background.
Invented by Erdal Arıkan in 2009.
First codes to achieve channel capacity of binary memoryless channels with explicit construction.
Encoding a involves polarizing channels to either completely noiseless or fully noisy channels.
COMPANY RESTRICTED
Encoder circuit for N=2

## Slide 4: Polar Codes background. Sample encoding in circuit for N = 8
# of info bits=4, code word size(N) = 8.
COMPANY RESTRICTED

## Slide 5: Polar Codes background.
As N becomes large, fraction of reliable bit indices approach the capacity of the channel.
Reliability indices selection is done based on the channel condition(SNR)
Many construction methods proposed such density evolution etc.
Still very complex to construct code on the fly.
5G standard(Huwaei contribution) proposes a heuristic low complexity polar code construction independent of channel condition.
This construction performs sufficiently good over a large range of SNR.

## Slide 7: PBCH Encoding FEC chain
COMPANY RESTRICTED

## Slide 8: Polar Encoding Chain in 5G
COMPANY RESTRICTED

## Slide 9: Measuring the latency. First step in code optimization.
Aim is to reduce the latency of encoding and decoding.
Requires accurate measurement of latency.
C++ STL chrono library provides high resolution time measurement, accuracy in the order of Nano seconds.
Accuracy guaranteed only in Linux platform.
Sample latency measurement snippet.
    high_resolution_clock::time_point start = high_resolution_clock::now();
    encodedData = PbchFecModule.fastEncode(mib, sfn, n_hf, iSSB, k0);
    high_resolution_clock::time_point end = high_resolution_clock::now();
COMPANY RESTRICTED

## Slide 10: Profiling the code. Second step in code optimization.
Helps to identify hotspots in the code.
Used open source profiler called perf.
Very low overhead and doesn’t require modification of binary file.
Data captured from hardware performance counters of the processor.
Accurately reflects the runtime behavior of the program.
COMPANY RESTRICTED

## Slide 11: Perf report
latency slide
COMPANY RESTRICTED

## Slide 12: Perf call graph
COMPANY RESTRICTED

## Slide 13: Polar Encoder Latency
Latency measurement of first functional implementation(MATLAB like) of Polar encoder.
K is the number of information bits, N is the numbers of bits at the encoder output, E is the number of bits after rate matching.
For the case of K = 130, N = 1024 and E = 846. Latency was 411 us without any optimizations.
Code rate at the output of encoder is 130/1024. After rate matching it is 130/846.
Perf report
COMPANY RESTRICTED

## Slide 14: Selecting reliability indices
K out of N indices for info bits position. This is in other words polar code construction. Specified in 5G spec.
In operation involves set union operations, searching operations, sorting operations.
Introduces highest latency in the whole FEC chain.
Costliest operation was searching for a
COMPANY RESTRICTED

## Slide 15: Optimization in selecting reliability indices
Before encoding data bits, K reliable positions out of N positions need to selected.
Interleaving pattern also need to be taken into account.
Process involves select K best positions out of N by searching through a list.
Low reliability indexes are removed from the list.
Searching, removing and erasing are very costly operations.
Use to take 176 us for just remove operations.
Costliest operation among all the operations in encoding.
COMPANY RESTRICTED

## Slide 16: Optimization of selection reliability indices
The aim is to avoid remove and erase operations.
Which involve costly memory deallocation and copy operations.
Efficient algorithm for selecting would be to find the element which needs to removed and mark it as removed, but don’t remove it.
This algorithm reduced the latency by 176 us.
Again the above algorithm can be further improved. since it involves many searching operations in an array of 1024 elements.
Total search time amounts to 40us. Which is highly undesirable.
Can we come up with a better method?
COMPANY RESTRICTED

## Slide 17: Optimization in selection reliability indices
Reliability index positions are constants. So why to search for them?
Why not build a lookup table whose value exactly gives position of the reliability index.
This method reduced the latency by 40 us which is good improvement.
Overall, latency improvement is by 216 us through efficient selection of reliability indices.
COMPANY RESTRICTED

## Slide 18: Polar encoding in tree structure.
Tree representation of polar encoding, For N = 8.
COMPANY RESTRICTED

## Slide 19: Optimization of Polar transform
Polar transform takes 55us.
Polar transform optimization.
  Avoiding memcpy operations.
  Using pointers to reduce memory allocation and deallocation.
  Using XOR operation in place of addition and mod operation.
  Latency reduced to 45us.
COMPANY RESTRICTED

## Slide 20: Polar transform function
Before
After
if (sizeIn==1)
{
dEncoded[m_index++] = *s;
}
else
{
UNS32 len = sizeIn/2;
UNS32 s1[len];
UNS32 s2[len];
std::copy(s, s+len, s1);
std::copy(s+len, s+sizeIn, s2);
for (UNS32 i = 0; i < len; ++i)
s1[i]= (s1[i] + s2[i]) % 2
recursiveMultG(s1,len,dEncoded);
recursiveMultG(s2,len,dEncoded);
}
if (sizeIn==1)
{
dEncoded[m_index++] = *s;
}
else
{
UNS32 len = sizeIn >> 1;
UNS32 *s1 = s;
UNS32 *s2 = s + len;
for (UNS32 i = 0; i < len; ++i)
s1[i]= (s1[i] ^ s2[i]);
recursiveMultG(s1,len,dEncoded);
recursiveMultG(s2,len,dEncoded);
}
COMPANY RESTRICTED

## Slide 21: SIMD implementation of Polar transform
Previous polar transform still takes 45us. Implementation can be further optimized using SIMD instructions.
In the previous implementation data is processed bit by bit.
Parallel processing of bits can be improved by making each set of 8/16/32/64 bits in to integers. This method improves the latency since multiple bits can be processed concurrently.
SIMD instructions support register size of 256 bits in AVX2 and 128 bits in AVX.
SIMD instructions allow processing of 256 bits in single instruction. Hence significantly improve the latency.
To get most out of SIMD, memory needs to be aligned.
COMPANY RESTRICTED

## Slide 22: Information bits grouping example
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
Last column only contains info bits
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
8 bits grouped as one integer.
Each row represents 8 bit integer representing one info bit.
Same idea can be extended to creating integers of 64 bits, so 64 info bits can processed concurrently.
COMPANY RESTRICTED

## Slide 23: SIMD processing of Information bits.
With previous method of grouping info bits, best case 64 bits info bits can be processed concurrently in 64 bit processor.
Still in case of 1024 bits, we have to do it 16 times in one node of polar encoding tree. Can we further reduce the number of operations?
SIMD instructions to rescue, with AVX2 256 bits and with AVX 128 bits can processed in a single operation.
For N=1024 bits, One stage can be processed with four AVX2 operations.
COMPANY RESTRICTED

## Slide 24: Sample SIMD code
inline void xor_256bit(void *operand1,void *operand2,void *destn)
{
  __m256i result;
  __m256i temp1 = _mm256_loadu_si256((__m256i*)operand1);
  __m256i temp2 = _mm256_loadu_si256((__m256i*)operand2);
  result = _mm256_xor_si256(temp1,temp2);
  _mm256_storeu_si256((__m256i*)destn, result);
}
vmovdqu 0x40(%rdi),%ymm0
vpxor (%rdi),%ymm0,%ymm0
vmovdqu %ymm0,(%rdi)
C/C++ sample
Corresponding Assembly
COMPANY RESTRICTED

## Slide 25: Sample polar encoder in circuit form, N = 16
COMPANY RESTRICTED

## Slide 26: Optimization of polar encoder.
One disadvantage of grouping information bits is that, when we need to perform polar transform in last 8 stages, Polar transform requires accessing 4,2 and 1 bits accessing these bits requires masking operation. Which further increase the latency.
These operations can be avoided by building a lookup table.
Building lookup table is equivalent to pruning encoder tree by grouping 8 leaf nodes to one.
Using lookup table reduces the latency in addition to avoiding masking operations.
COMPANY RESTRICTED

## Slide 27: Unrolling the recursive function.
Recursive implementation looks pretty neat however it has significant overhead.
Every recursive call requires jump instruction and allocation of new stack frame.
This overhead can be avoided if encoder is implemented in non recursive way.
As maximum N specified in 5G spec is 1024, We can specialize the polar transform function for different values N. i.e 1024,512 etc. Correct function is chosen based on the value of N, which further calls N/2 specialized functions. All these functions are inline functions, Which makes encoder branch free implementation.
COMPANY RESTRICTED

## Slide 28: Pictorial representation of branch free encoder. For N = 64
Unrolled decoder in tree form
inline void bitMultG64(uint8_t *s, uint8_t *dEncoded)
{
//Here s is 64 bits, Divided to 32 bits each.
uint32_t *s1 = (uint32_t *) s + 1;
uint32_t *s2 = (uint32_t *) s;
*s1 = *s1 ^ *s2;
bitMultG32((uint8_t *) s1, dEncoded);
bitMultG32((uint8_t *) s2, dEncoded);
}
inline void bitMultG32(uint8_t *s, uint8_t *dEncoded) {
//Here s is 4 bytes, Divided to two bytes each.
uint16_t *s1 = (uint16_t *) s + 1;
uint16_t *s2 = (uint16_t *) s;
*s1 = *s1 ^ *s2;
bitMultG16((uint8_t *) s1, dEncoded);
bitMultG16((uint8_t *) s2, dEncoded);
}
COMPANY RESTRICTED

## Slide 29: Latency of polar transform.
With all the above optimizations avoiding copy operations, bits grouping, SIMD instructions, Lookup table and unrolled branch free implementation. The latency of polar transform is reduced significantly from 55us to 1.5us for N = 1024.
In other words current implementation of polar transform can encode 1024 bits with in 1.5 us in worst case scenario, Best case scenario 0.7us.
COMPANY RESTRICTED

## Slide 30: Efficient CRC calculation
Another significant latency contributor to PDCCH Encoding chain is CRC calculation. On the fly CRC calculation takes 8us with CRC24.
In optimized implementation, a lookup table is built. In which 24 bit CRC is calculated for all combinations 8bits and stored in a look up table.
For more than 8 bits info bits, CRC read from lookup table for chunks of 8 bits and is combined to generate CRC for the whole data block.
Optimized implementation takes 0.8us for 64 information bits.
COMPANY RESTRICTED

## Slide 31: Other optimizations to FEC chain
  Using compiler primitives to help the branch predictor to reduce branches.
  Aligning memory to 32 bytes so that compiler can generate SIMD code wherever it is possible.
  Avoiding costly operations such as division and multiplications instead using right shift and left shift operations.
  Avoiding dynamic memory allocations.
  Manual loop unrolling to reduce the branches (Jumps) in the code.
  Implementation log2 function using bit wise operations.
  With all the above optimizations, Latency of the whole FEC chain is reduced from 411us to 20us.
COMPANY RESTRICTED

## Slide 32: TODO for Encoding
Optimizing the cache accesses. Probably prefetching the data from cache?
little difficult , Since it is hard to identify which part of the code is experiencing most cache misses.
COMPANY RESTRICTED

## Slide 33: Current work. Decoder implementation with SIMD.
Have done literature survey related to decoding algorithms.
Three different decoding algorithms are popular, Successive cancellation(SC), Simplified Successive Cancellation(SSC) and Fast SSC.
Among three, Fast-SSC is the fastest decoder.
Currently, implementing the Fast SSC decoding algorithm.
COMPANY RESTRICTED

## Slide 34: Research directions
Fastest algorithm i.e Fast-SSC identifies repetition and SPC component codes in polar code. These codes are decoded immediately without traversing the remaining tree.
  Investigate whether it is possible to identify any other type of component code which allows faster decoding.
Hard decision decoding is just performing polar transform on received bits after threshold detection. Try performing soft decision decoding for lower level nodes and hard decoding for higher level nodes, This reduces the decoding latency but increases the BER.
  Investigate BER versus level of hard decision decoding in tree. Can we trade a BER for low latency?
Any other ideas and Suggestions for improvement are welcome.
COMPANY RESTRICTED

## Slide 35: References
E. Arıkan, “Channel polarization: A method for constructing capacity-achieving codes for symmetric binary-input memoryless channels,” IEEE Trans. Inform. Theory, vol. 55, pp. 3051–3073, July 2009.
Sarkis, G., & Gross, W. J. (2013). Increasing the throughput of polar decoders. IEEE Communications Letters, 17(4), 725–728.
Alamdar-Yazdi, A., & Kschischang, F. R. (2011). A simplified successive-cancellation decoder for polar codes. IEEE Communications Letters, 15(12).
Low-Latency Software Polar Decoders, Pascal Giard, Claude Thibeault, Warren J. Gross.
A Practical Introduction to Polar Codes (A very simple tutorial for beginners) Harish Vangala, Yi Hong, and Emanuele Viterbo, Monash University, Australia.
3rd Generation Partnership Project;
Technical Specification Group Radio Access Network; NR; Multiplexing and channel coding (Release 15).
COMPANY RESTRICTED

## Slide 36: Thanks
COMPANY RESTRICTED